## Slide 1: February 2025 Battery FIAMM – Riyadh L3
ALSTOM RS
2025-02-10
Caio Oliveira

## Slide 2: MTBF – Instantaneous
Total of 276 batteries in operation
Total time of 11,690,712 hours

## Slide 3: MTBF – Previous Results #1
MTBF for the last 90 days (Aug to Oct/23) was 65,643 hours.
The demonstrated Cumulative MTBF (Up to Oct/23) for the fleet was 48,262 hours.

## Slide 4: MTBF – Previous Results #2
MTBF for the last 90 days (May to Jul/24) is 61,109 hours.
The demonstrated Cumulative MTBF (Up to Jul/24) for the fleet is 47,036 hours.

## Slide 5: MTBF – Latest Result
MTBF for the last 90 days (Jul to Sep/24) is 54,617 hours.
The demonstrated Cumulative MTBF (Up to Sep/24) for the fleet is 43,317 hours.

## Slide 6: MTBF – Latest Result
MTBF for the last 90 days (May to Jul/24) is 54,617 hours.
The demonstrated Cumulative MTBF (Up to Jul/24) for the fleet is 43,317 hours.

## Slide 7: MTBF – Previous Results
New failure database – 41 Events
MTBF Urgent – 56,290 hours
  Battery Controller Failure
  Battery Main Contactor Failure
  Charge Regulator Failure
  Communication Error
  Heating System Fault
  High Battery Voltage
  Low Battery Voltage
  String Voltage Unbalance
  Temperature Probe Error
MTBF Non-Urgent - 286,139 hours
  Fault Clear itself
  String Voltage Unbalance
Need Same Day Action | 25
Battery Controller Failure | 2
Battery Main Contactor Failure | 1
Communication Error | 3
High Battery Voltage | 1
Low Battery Voltage | 2
String Voltage Unbalance Alarm | 16
No Immediate Action | 16
String Voltage Unbalance Warning | 16

## Slide 8: MTBF – Latest Result
New failure database – 27 Events
MTBF Urgent – 209 Failures – 50,778 hours
  String Voltage Unbalance
  Charge Regulator Failure
  Low Battery Voltage
  Fault Clear itself
  Battery Controller Failure
  Heating System Fault
  High Battery Voltage
  Communication Error
  Temperature Probe Error
  Battery Main Contactor Failure
MTBF Non-Urgent - 36 Failures - 294,800 hours
  String Voltage Unbalance